# Preflight Cockpit (172F – 8716U)

Aircraft docs (ARROW)	Check

Weight & Balance	Check

Fire Extinguisher	Check

Parking Brake	Set

Control wheel lock	Remove

Hobbs/Tach	Check/Record

Oil Change/ADs	Check Current

Ignition	Off

Avionics Power Switch	Off

Master Switch	On

Fuel quantity indicators	Check

Flaps 	Extend

Lights	On/Check/Off

Stall warning	Check

Master Switch	Off

Fuel Strainer	Pull

# Fuselage and Empennage

Baggage Door	Closed & Locked

Tail Tie-Down	Disconnect

Control surfaces	Free & Secure

Trim Tab	Check Security

Antennas	Check Security

# Right wing

Wing tie-down	Disconnect

Aileron	Free and Secure

Flaps	Secure

Main wheel tire(24psi)	Inflated/Cond

Brakes	Pads/Leaks

Fuel tank sump	Sample

Fuel quantity	Check

Fuel filler cap	Secure

(Phillips 66 X/C 20W50)

# Nose

Air inlet covers	Remove

Propeller and spinner	Check

Air intake 	Check

Carburetor air filter	Check

Nose wheel strut & tire(26psi)	Check

Static source opening	Check

Engine oil level (6 Quarts)	Check

Engine oil cap	Secure

# Left Wing

Wing tie-down	Disconnect

Aileron	Free and Secure

Flaps	Secure

Main wheel tire(24psi)	Inflated/Cond

Brakes	Pads/Leaks

Fuel tank vent open	Check

Fuel tank sump	Sample

Fuel Quantity	Check

Fuel Filler cap	Secure

Pitot tube	 Check

Pitot flap	Free to move

# Before starting engine

Towbar	Stowed

Preflight inspection	Complete

Passenger Briefing	Complete

Seats, belts	Adjust & Lock

Doors 	Closed & Locked

Brakes 	Test & Set

Circuit breakers	Check In

Avionics Power Switch	Off

Fuel Selector Valve	Both

# Starting Engine

ENGINE COLD

Throttle	Open 1/8 inch

Mixture 	Rich (IN)

Carb heat	Cold (IN)

Prime	As required; locked

Propeller area	Clear

Master Switch	On

Beacon 	On

Ignition	Start

ENGINE WARM

Throttle	Open 1/8 inch

Mixture	Lean (OUT)

Prime	As required; locked

Propeller area	Clear

Master Switch	On

Beacon	On

Ignition	Start

Mixture	Full Rich

Throttle	Adjust 1000 rpm

Oil Pressure	Check normal

Alternator Switch	On

Avionics Master Switch	On

Radios	On

Transponder	1200 ALT

Flaps	Up

Ammeter 	Check

Heading Indicator 	Set

ATIS/AWOS/ASOS 	Obtain

Altimeter 	Set

OK to Taxi	Confirmed

# Before Takeoff

Parking brake	Set

Cabin doors	Closed & Locked

Seats, belts	Adjust & Lock

Flight controls	Free & Correct

Instruments	Set

Fuel Quantity	Check

Mixture	Rich (IN)

Fuel Selector Valve 	Both

Elevator Trim	Set for TAKEOFF

Throttle	1600 rpm

Magnetos (75 rpm max dif)	Check

Suction gage 	Check

Engine Instruments	Check

Alternator	Check

Mixture	Set for Density Alt

Carb heat	On

Throttle	Idle

Carb Heat	Off (In)

Throttle Friction Lock	Adjust

Strobe Lights	On

Radios/Avionics	Set

Transponder	Verify

Flaps	Set for Takeoff (00-100)

Parking Brake	Release

Windows	Closed

# Standard Takeoff

Flaps	Up

Carb heat	Off (In)

Trim	Set for TAKEOFF

Throttle	Full

Tach, oil, airspeed	Check

Elevator	Rotate at 60 MPH

Climb	80 MPH

# Cruise

Pitch	Set

Lights	As Required

Throttle	As required

Trim	Set

Mixture 	Adjust

Fuel Selector Valve	Both

>5000 ft elev	Left/Right

# Pre-landing checklist

Fuel selector	On Both

Mixture	Rich

Carb Heat	On

Seatbelts	Fastened

ATIS	Checked

# Approach

Flight instruments	Ckd & Set

Radios	Checked

Carb Heat	On (Out)

Mixture	Rich

Landing light 	On

Airspeed 	70-80 MPH (Flaps Up)

65-75 MPH (Flaps Dn)

# After landing

Flaps	Up

Carb Heat	Cold (In)

# Parking

Lights	Off

Avionics	Off

Throttle	Idle

Mixture 	Cut-off

Ignition switch	Off

Master switch	Off

# Securing the aircraft

Control Lock	Install

Air Inlet Cover	Install

Hobbs/Tach	Record

Door/Window	Secure

Tie-downs	Secure

Doors/Baggage Door	Locked

BUGS CLEANED OFF WINDSHIELD AND WINGS

Oil Added 	Recorded

Flight Circle	Aircraft Checked-In

Aircraft Key	In Lockbox

Last updated 8/24/19

# Short field take-off

Take-off checklist	Complete

Flaps	10(

Taxi	Max runway

Brakes	Set and hold

Throttle 	Full

Brakes	Release

Climb	65 MPH

Flaps	Retract

# Short field landing

Pre-landing check	Complete

Approach	67 MPH

Flaps	40(

Throttle	Maintain glide

Touchdown	Power Off

Flaps	Up

Elevator 	Full up

Braking	Heavy as required

# Soft field take-off

Take-off checklist	Complete

Flaps	10(

Taxi	Keep rolling

Liftoff	ASAP

Level	Stay in ground effect

Climb	80 MPH

Flaps	retract

# Soft field landing

Pre-landing check	Complete

Throttle	1500 RPM

Flaps	40(

Airspeed	69 MPH

Touchdown	Main first, softly

Landing roll	Nose wheel up

Elevator	Up

Braking	As required

# Go-around

Throttle	Full

Carb Heat	Cold (In)

Flaps	20(

Climb 	65 MPH

Flaps	10(

Climb	80 MPH

Flaps	Up

# Engine failure

TAKEOFF

Throttle	Idle

Brakes	Apply

Flaps	Retract

Mixture	IDLE cut-off

Fuel selector valve	Off

Ignition	Off

Master switch	Off

# AFTER TAKEOFF

Airspeed	80 MPH (flaps UP)

Mixture 	Idle Cut-off

Fuel selector valve	Off

Ignition	Off

Flaps 	As Required

Master switch	Off

Cabin Doors	Unlatch

Land	Straight Ahead

# DURING FLIGHT

Airspeed 	80 MPH

# LOOK FOR A FIELD

Fuel selector valve	Both

Primer 	In & Locked

Mixture	Rich

Ignition	BOTH (or START)

Airspeed	70-80 MPH (flaps UP)

65-75 MPH (flaps DN)

Mixture 	Idle Cut-off

Fuel selector valve	Off

Ignition	Off

Flaps 	As Required

Mayday	Transmit 121.5

Mayday	Squawk 7700

Master switch	Off

Cabin Doors	Unlatch

Touchdown	Tail Low

# Carburetor Icing

Throttle	Full

Carb Heat	On (Out)

Mixture	Adjust

# Engine Roughness

Magnetos	Check

Mixture	Lean as necessary

Primer	Check in & locked

# Engine Fire during start

Crank	Continue

Power	1600 RPM (2 min)

Engine	Shut down and inspect

# Engine Fire during flight

Mixture 	Idle Cut-off

Fuel selector valve	Off

Master Switch	Off

Alternator Switch	Off

Cabin Heat/Air	Off

Airspeed	120 MPH

Electrical Fire during flight

Master Switch	Off

Ignition Switch	On

All other switches	Off

Circuit Breakers	Ident Bad Circuit

Master Switch	On

Electrical Switches	On

(One at a time)

# Spin Recovery

Ailerons	NEUTRAL

Throttle	IDLE

Rudder	Full opposite

Control wheel	Full forward

Rudder control/wheel	Neutral

Pitch	Level

# Text boxes

V-Speeds (MPH)

| Rotate | Vr | 60 |
| --- | --- | --- |
| Normal Climb Out | Vclmb | 80-90 |
| Max angle (Sea Level) | Vx | 65 |
| Max angle (10,000 ft) | Vx | 71 |
| Climb rate (Sea Level) | Vy | 80 |
| Climb rate (10,000 ft) | Vy | 77 |
| Maneuver | Va | 95-122 |
| Flaps | Vfe | 100 |
| Normal max | Vno | 140 |
| Never exceed | Vne | 174 |
| Stall (clean) | Vs | 57 |
| Stall (land) | Vso | 49 |
| Final Approach | Flaps | 65-75 |
|  | No flaps | 70-80 |
| Max Glide | 80 |

Useable Fuel Capacity 39 Gallons

Alpha

Bravo

Charlie

Delta

Echo

Foxtrot

Golf

Hotel

India

Juliet

Kilo

Lima

Mike

November

Oscar

Papa

Quebec

Romeo

Sierra

Tango

Uniform

Victor

Whiskey

Xray

Yankee

Zulu

Light Signals:

| Signal | On Ground | In Flight |
| --- | --- | --- |
| Steady Green | Takeoff | Land |
| Flashing Green | Taxi | Return to land |
| Steady Red | Stop | Give way |
| Flashing Red | Clear runway | Do not land |
| Flashing White | Return to ramp | -- |
| Red/Green alternating | WARNING – USE CAUTION |